# Atmospheric Mercury – Global Biogeochemical

# Cycles, Sources, and Sinks

#### Richard D. Doctor, John A. Taylor, and Jack D. Shannon

Argonne National Laboratory

9700 S. Cass Avenue

Argonne, Illinois  60439

#### January 2000

The submitted manuscript has been created by the University of Chicago as Operator of Argonne National Laboratory (“Argonne”) under Contract No. W-31-109-Eng-38 with the U.S. Department of Energy.  The U.S. Government retains for itself, and others acting on behalf, a paid-up, nonexclusive, irrevocable worldwide license and said article to reproduce, prepare derivative works, distribute copies to the public, and perform publicly and display publicly, by or on behalf of the Government.

Contents

1.	Overview	1

2. 	Terrestrial Sequestration of Mercury by the Biosphere	1

3. 	Preindustrial Mercury Flux Estimates	2

4. 	Sources of Anthropogenic Mercury Emissions	2

4.1 	Coal and Increasing Mercury Emissions from Market Shifts to Western Coals	3

4.2	Studies of Mercury Emissions from Coal-fired Power Plants	3

4.3	Studies of Mercury Emissions from Smelters	3

4.4	Studies of Mercury Emissions from Chloralkali Plants, MSW Sludge, and

Gold Refining	4

4.5	Evidence for High Foreign Mercury Emissions	4

4.6	Open Questions on Anthropogenic Mercury Emissions	4

5. 	Atmospheric Modeling	4

5.1	Eulerian Mercury Transport Models	5

5.2	Lagrangian Mercury Transport Models	5

6.	Proposed Global Modeling Studies	6

7.	Conclusions	6

Acknowledgments	7

References	7

## 1.	Overview

Measurements of atmospheric mercury (Hg) at remote locations, such as the North Atlantic, confirm that the levels of mercury in the global atmosphere are increasing.  In spite of considerable effort, estimating the global movement of mercury through the environment is difficult.  However, anthropogenic emissions of mercury are at least double those from natural sources and are of such magnitude that they cannot be attributed to natural sources alone [Fitzgerald et al. 1998].  Emissions are considered to be increasing in Asia and decreasing in North America and Europe.

On the basis of current estimates of the atmospheric burden and the flux of mercury to the atmosphere, we can estimate the lifetime of atmospheric elemental mercury (Hgº) to be around one year, while the lifetime of atmospheric divalent mercury (Hg-II) to be one to three days.  A lifetime of one year implies that Hgº is a global pollutant, while the much shorter lifetime of Hg-II implies that it is a local to regional pollutant.  Therefore, to understand the link among emissions, emissions speciation, and final deposition, we need to take a regional to global approach.  Accordingly, in this paper, we propose that the global biogeochemical cycle of mercury be modeled and studied in detail.  We suggest that an approach combining state-of-the-art techniques for inventory estimation with high-resolution global tracer transport modeling is required to reduce the fundamental scientific uncertainties associated with the release, transport, transformation, and ultimate removal through deposition of mercury to the land and ocean.

In the following sections, we review the natural cycle of atmospheric mercury, industrial and natural emission sources, and atmospheric modeling studies.  In Section 6, we propose a global modeling study of the biogeochemical cycles of atmospheric mercury.

2. 	Terrestrial Sequestration of Mercury by the Biosphere

Considering the global biogeochemical mercury cycle, Mason et al. [1994] has shown that the atmosphere and ocean are in rapid equilibrium with respect to atmospheric mercury.  The evasion of Hg0 from the ocean matches the deposition of mercury, mostly Hg-II, from the land.  Mason pointed to strong evidence that biological processes produce Hg0 from the biological reduction of Hg-II, although the precise nature of these processes is poorly known.  Numerous laboratory and field studies strongly support the conclusion that the action of phytoplankton in sunlight converts HG-II to Hg0.

While the oceanic inventory of mercury is more than twice that of the atmospheric inventory (54 Mmol vs. 25 Mmol where Mmol is 103 kg-moles), mercury is deposited into ocean sediments at a rate of less than 1 Mmol/yr.  In contrast, mercury is deposited onto land at a rate of 25 Mmol/yr with a net re-emission to the atmosphere from soils holding mercury of 5 Mmol/yr.  Hence, soils accumulate mercury.  The current inventory on land is estimated to be 5,000  Mmol.

Anthropogenic emissions of the Hg-II form of mercury have large local impacts, and Mason suggests that 50% of the mercury deposits “locally.”  Hence, the deposition of mercury to terrestrial environments is disproportionately high; 30% of the earth’s surface receives 60% of the atmospheric deposition.  The conclusion from a biogeochemical perspective is that ocean life works very hard to move Hg0 from the ocean for sequestration in the terrestrial biosphere.

3.	Preindustrial Mercury Flux Estimates

Mason et al. [1994] estimated pre-industrial terrestrial fluxes to the atmosphere from natural sources to be 5 Mmol/yr, with a matching deposition rate of 5 Mmol/yr.  At the same time, preindustrial pelagic fluxes to the atmosphere were estimated to be 3 Mmol/yr, with a matching deposition rate of 3 Mmol/yr.  Mason et al. believe that both the atmospheric and oceanic inventories of mercury have increased 300% from preindustrial levels.  The current atmospheric mercury inventory is 25 Mmol; in contrast, the preindustrial level is estimated to have been 8 Mmol.  The current oceanic mercury inventory is 54 Mmol; in contrast, the pre-industrial level is estimated to have been 18 Mmol.  The rate of mercury discharge to the oceans attributable to the flow of surface waters from the land surface is also assumed to be 300% higher than the preindustrial rate (~0.3 Mmol/yr), and ocean sedimentation rates are assumed to be 300% higher than preindustrial rates (~0.3 Mmol/yr).

4. 	Sources of Anthropogenic Mercury Emissions

For the United States, a recent U.S. Environmental Protection Agency (EPA) inventory produced a total for all the domestic mercury emissions of 144 Mg/yr (or 0.7 Mmol/yr) [EPA, 1997].  Anthropogenic emissions of Hgº and Hg-II are believed to be of similar order, but proper speciation of mercury emissions remains a vexing issue.  These values seem easier to reconcile with the estimates by Pirrone et al. [1996].  The EPA reports that point sources account for 98% of emissions.  However, other U.S. inventories have somewhat reduced the contribution from point sources and given more weight to nonpoint sources [Pai et al. 1998].  Pai et al. concluded that point sources accounted for about 89% of the total 48-state mercury emissions of 146.4 Mg/yr.  These point sources are allocated as follows:  46% are from coal burning, 19% are from municipal waste combustion, 10% are from medical waste combustion, 10% are from manufacturing (with the production of chlor-alkali compounds as the leading cause), and 7% are from fuel oil combustion.

Mason et al. (1994) estimated that 50% of mercury emissions would deposit locally.  The link between mercury levels and local sources of mercury in both Europe and North America frequently appears in the literature [Landers et al. 1998].  The current best estimate of an average worldwide background deposition rate is ~16 (gm/m2(yr, on the basis of four reports for North America and Europe.  Recent studies measuring mercury deposition rates of 19 (gm/m2(yr [Benoit et al. 1998] are consistent with this value.

Mercury sampling at Alaskan sites provides an integrated sample of mercury pollution in the Northern Hemisphere; the results of sampling from these sites show that global mercury emissions have not abated [Engstrom and Swain, 1997].  It is likely that reduced mercury emissions from regional sources reduce inputs to Midwestern lakes.  Decreased emissions in the United States are probably the result of the reduced industrial use of mercury, the use of pollution-control technologies that incidentally capture mercury, a shift from coal to natural gas for commercial and residential heating, and a decrease in uncontrolled waste incineration.  Increased stack height and other factors that favor long-distance transport are possible explanations for this trend.

4.1	Coal and Increasing Mercury Emissions from Market Shifts to Western Coals

Since the largest single source of mercury is the combustion of coal, what can be said about mercury levels from this resource?

When neutron activation analysis was used to detect mercury in standard coals in the Argonne Premium coal bank [Vorres 1990], there was a pattern of grade vs. mercury level that requires considerable knowledge of the coal basin to interpret consistently [Richaud et al. 1998].  Hence, while the mercury values obtained for the given samples are accurate, many more channel samples need to be analyzed to be certain that the specific premium coal samples were typical of the larger population.

Among the eastern coals, the Lewiston-Stockton (WV) high-volatile bituminous mercury level is 0.178 (-gm/gm coal, which essentially matches Illinois #6 high-volatile bituminous at 0.181 (-gm/gm coal.  However, the Upper-Freeport (PA) medium-volatile bituminous coals show the highest measured mercury levels:  1.748 (-gm/gm.  Pocahontas #3 (VA), a low-volatile bituminous coal, has a mercury level of 0.112 (-gm/gm.  The western low-sulfur coals were represented by Wyodak-Anderson (WY), a subbituminous coal with a mercury content of 0.292 (-gm/gm.  If mercury in the premium coal samples accurately reflects their respective basins, the recent large market movement toward the use of Western coals to displace Illinois basin coals suggests that mercury emissions have increased.  For every ton of Illinois coal displaced by moist, low-heating value Wyoming coal, mercury emissions from that point source may have increased by 210%.

### 4.2  	Studies of Mercury Emissions from Coal-fired Power Plants

Mercury concentrations were surveyed in fish from twenty-three ponds in the vicinity of a 543 MW coal-fired power plant in Dickerson, Maryland  [Pinkney et al. 1997].  A stratified random sampling design was used to select ponds within zones delineated by a concentric area mapped at 3, 7, 10, and 15 km from the plant.  For each pond, mercury concentrations were measured by atomic absorption spectrometry in sunfish (bluegill or green sunfish) in all ponds and largemouth bass.  Mean mercury concentrations in the ponds ranged from 0.01 to 0.38 ppm for sunfish and 0.04 to 0.43 ppm for bass.  However, the observed pattern of mercury bioaccumulation did not match the pattern predicted by a wet deposition model.

### 4.3 	Studies of Mercury Emissions from Smelters

One group [Ames et al. 1998; Olmez et al. 1998] identified atmospheric particulates by origin and found that approximately 55% of the fine particulate mercury originated from smelters in Ontario and Quebec, and 25% originated from a mixture of regional sources in the Midwestern United States.  The source identification results for the fine aerosols were confirmed by examining back-projected, mixed-layer wind trajectories.  Significant declines in fine-particulate mercury concentrations were attributed to the installation of particulate controls at one or more of the copper smelters.

4.4  	Studies of Mercury Emissions from Chloralkali plants, MSW Sludge, and Gold Refining

Reports [Lodenius, 1998] on the dry and wet deposition near a Finnish chlor-alkali plant using the moss-bag technique yielded an estimate of net deposition of 480 (gm/m2(yr.  Two-thirds of the deposition was dry and one-third wet.  This deposition is thirty times the background level.  Even higher impacts have been reported around chloralkali plants in Portugal [Inacio et al. 1998].

According to Carpi et al. [1997], using municipal sewage waste as a soil amendment results in an emission rate of 0.0001 (gm/m2(hr mercury.  If this rate could be maintained day and night throughout the year, which is not possible because there is only a fixed amount of mercury in the soil, it would result in an annual impact of 876 (gm/m2(yr [Malm et al. 1998].  Reports of bioaccumulation in plants near an urban site working on gold-refining and gold shops found mercury to be three hundred times in excess of background after forty-five days.

### 4.5 	Evidence for High Foreign Mercury Emissions

Reports of anthropogenic mercury emissions nearly double those from the United States have been attributed to Siberia.  A recent investigation of natural and anthropogenic mercury emissions from Siberia found quantitative estimates of mercury emissions of 0.32 Mmol/yr for natural sources and 1.54 Mmol/yr for anthropogenic sources [Vasiliev et al. 1998].

4.6	Open Questions on Anthropogenic Mercury Emissions

The 1997 EPA mercury balance is not completely accurate and will likely shift to show a greater influence from manufacturing as the inventory is refined.  Primary mercury production and processing, coke production, and oil refining were noted, but they were not included in the 1997 report because insufficient information was available.  These are certain to be significant sources that need to be investigated and quantified further.

5.	Atmospheric Modeling

Atmospheric modeling studies have been undertaken at the local/regional scale, primarily in the United States.  In the following sections, we briefly review both Eulerian and Lagrangian approaches to modeling atmospheric mercury and its deposition.

### 5.1	Eulerian Mercury Transport Models

Pai et al. [1998] developed geographically resolved estimates of annual average mercury emission rates from current anthropogenic sources in the 48 contiguous United States.  These estimates were made by applying emission factors to individual facility operating data and to county-wide source activity levels.  Emissions were apportioned to an Eulerian modeling grid system by using point source coordinates and the fractions of county areas in each grid cell.  Most of the emissions in the inventory are from the combustion of mercury-containing fossil fuels and municipal waste, which are located primarily in the mid-Atlantic, Great Lakes, and Southeast states.  Major uncertainties in the emission factors used to develop the estimates need to be resolved.

Peterson et al. [1998] are developing a comprehensive mercury model system by using the Eulerian reference frame of the Acid Deposition and Oxidant Model (ADOM) to study the regional transport of atmospheric mercury species.

5.2	Lagrangian Mercury Transport Models

The Advanced Statistical Trajectory Regional Air Pollution (ASTRAP) model, developed at Argonne, has been used to model the deposition of mercury to the Great Lakes Basin [Shannon and Voldner, 1995].  The Regional Lagrangian Model of Air Pollution (RELMAP) is being used to simulate the emission, transport and diffusion, chemical transformation, and wet and dry deposition of elemental mercury gas, divalent mercury gas, and particulate mercury from various point and area-source types for the seven point-source categories [Bullock et al. 1998].

Schroeder and Munthe [1998] advocates intercompartmental (air-water/soil/vegetation) transfer and biogeochemical cycling of mercury in an effort to improve current models.

Recently the results of an EPRI-funded study looking at the global transport of atmospheric mercury using the GISS 8x10 degree chemical transport model were reported [Shia et al. 1999].  Their model considered mercury chemistry, deposition, and emissions.  They concluded that the global atmospheric transport of mercury is important to the regional deposition in North America.  Mercury is a transboundary issue.  They also observed that aqueous chemistry in water droplets may play an important role in determining mercury’s atmospheric lifetime and deposition.  Finally, they noted the need to further reduce the uncertainties in model parameters in order to be able to reliably estimate source and receptor relationships.   This effort is encouraging because the call for reducing uncertainties in the model parameters in fact focuses on explicitly linking the highly significant biological contributions to atmospheric mercury emissions.

6.	Proposed Global Modeling Studies

Global modeling studies provide critical information for determining the sources and sinks of trace gases [Mulquiney et al. 1993].  Global models have been used extensively to study the biogeochemical cycles of greenhouse gases, such as CO2 [Taylor 1989, 1990, 1995, 1996; Taylor and Lloyd 1992; Farquhar et al. 1993; Klinger et al. 1995; Taylor et al. 1996], CH4 [Taylor et al. 1991], and N2O [Taylor 1992; Bouwman et al. 1995, 1996], as well as other trace compounds, such as CO [Erickson and Taylor 1992], with relatively long atmospheric lifetimes.

We propose to undertake a study that will incorporate our understanding of both the natural biogeochemical cycles of mercury with estimates of the global industrial sources and sinks of mercury into a high-resolution global Lagrangian atmospheric tracer transport model [Taylor 1989].  Previously, this modeling system was applied extensively to the study of biogeochemical cycles of greenhouse gases (as noted above).  We seek to understand, at the global scale, the natural biogeochemical cycle and quantity of mercury, the anthropogenic release of mercury, and its influence on the natural mercury cycle.  Finally, we propose to investigate the mechanisms producing the observed increase in atmospheric mercury so that we might be able to predict future atmospheric mercury levels.

We briefly outline the key research activities:

- Develop a detailed global emissions inventory for mercury from anthropogenic sources for inclusion in the global tracer transport model.

- Develop parameterizations for the exchange of mercury between the oceans, land surface, and biosphere for inclusion in the global tracer transport model.

- Develop mercury atmospheric chemistry parameterization for inclusion in the global tracer transport model.

- Perform multiyear global tracer transport model integrations for comparison with observations.  Study the atmospheric transport, chemistry, sources, and sinks of mercury.  Quantify sources and sinks and atmospheric lifetime.

- Investigate the release of atmospheric mercury from individual point sources and regions and its transport and ultimate removal from the atmosphere (i.e., the relationship between sources and sinks of atmospheric mercury from a global perspective).

7.	Conclusions

Levels of atmospheric mercury are increasing in the remote troposphere, far from known sources.  Given that global mercury emissions are likely to be increasing rapidly in the future, improving our scientific understanding of the global biogeochemical cycle of mercury is urgently needed.  To improve our understanding of the biogeochemical cycle of atmospheric mercury, we propose to develop an integrated global model that will incorporate the natural mercury cycle and the influence of the anthropogenic release of mercury.  This will allow us to reduce the scientific uncertainties associated with the sources and sinks of atmospheric mercury and test assumptions about the mechanisms producing the observed increase in atmospheric mercury.  Mercury is a global problem that needs to be addressed from a global perspective.

## Acknowledgments

The work reported here was supported by the U.S. Department of Energy, Assistant Secretary for Science, under Contract W-31-109-Eng-38.

References

Ames, M., Gullu, G., and Olmez, I., 1998 (March).  “Atmospheric mercury in the vapor phase, and in fine and coarse particulate matter at Perch River, NY,” Atmospheric Environment, 32:5, pp. 865–872.

Benoit, J. M., Fitzgerald, W. F., and Damman, A. W. H., 1998 (Aug.).  “The biogeochemistry of an ombrotrophic bog:  Evaluation of use as an archive of atmospheric mercury deposition,” Environmental Research, 78:2, pp. 118–133.

Bouwman, A. F., and Taylor, J. A., 1996.  “Testing high-resolution nitrous oxide emission estimates against observations using an atmospheric transport model,” Global Biogeochemical Cycles, 10, pp. 307–318.

Bouwman, A. F., van Dam, D., van der Hoek, K. W., Olivier, J. G. J., and Taylor, J. A., 1995.  “Modelling of soil emissions of nitrous oxide for global studies,” National Institute of Public Health and Environmental Protection, Bilthoven, the Netherlands, Report No. 773004006, 48 pp.

Bullock, O. R., Brehme, K. A., and Mapp, G. R., 1998 (June 10).  “Lagrangian modeling of mercury air emission, transport and deposition:  An analysis of model sensitivity to emissions uncertainty,” Science of the Total Environment, 213:1-3, pp. 1–12.

Carpi, A., Lindberg, S.E., Prestbo, E. M., and Bloom, N. S., 1997 (Nov.).  “Methyl mercury contamination and emission to the atmosphere from soil amended with municipal sewage sludge,” Journal of Environmental Quality, 26:6, pp. 1650–1655.

Engstrom, D. R., and Swain, E. B., 1997 (April).  “Recent declines in atmospheric mercury deposition in the upper Midwest,” Environmental Science & Technology, 31, 4, pp. 960–967.

##### EPA, 1997 (Dec.).  “Mercury study report to Congress; Vol. II:  An inventory of anthropogenic mercury emissions in the United States,” EPA-452/R-97-004:  http://www.epa.gov/ttnuatw1/112nmerc/mercury.html.

Erickson III, D. J., and Taylor, J. A., 1992.  “3-D tropospheric CO modelling:  The possible influence of the ocean,” Geophysical Research Letters, 19, pp. 1955–1958.

Farquhar, G. D., Lloyd, J., Taylor, J. A., Flanagan, L. B., Syvertsen, J. P., Hubick, K. T., Wong, S. M. C., and Ehleringer, J. R., 1993.  “Vegetation effects on the isotopic composition of oxygen in atmospheric CO2,” Nature, 363:439–443.

Fitzgerald, W. F., Engstrom, D. R., Mason, R. P., and Nater, E. A., 1998 (Jan. 1).  “The case for atmospheric mercury contamination in remote areas,” Environmental Science & Technology, 32:1, pp. 1–7.

Inacio, M. M., Pereira, V., and Pinto, M. S., 1998 (Sept.).  “Mercury contamination in sandy soils surrounding an industrial emission source (Estarreja, Portugal),” Geoderma 85:4, pp. 325–339.

Klinger, L. F., Taylor, J. A., and Franzen, L. G., 1995.  “The potential role of peatland dynamics in Ice-Age initiation,” Quaternary Research, 45, pp. 89–92.

Landers, D.H., Gubala, C., Verta, M., Lucotte, M., Johansson, K., Vlasova, T., and Lockhart, W.L., 1998 (March).  “Using lake sediment mercury flux ratios to evaluate the regional and continental dimensions of mercury deposition in arctic and boreal ecosystems,” Atmospheric Environment, 32:5, pp. 919–928.

Lodenius, M., 1998 (June 10).  “Dry and wet deposition of mercury near a chlor-alkali plant,” Science of the Total Environment, 213:1–3, pp. 53–56.

Malm, O., Fonseca, M. D., Miguel, P. H., Bastos, W. R., and Pinto, F. N., 1998 (June).  “Use of epiphyte plants as biomonitors to map atmospheric mercury in a gold trade center city, Amazon, Brazil,” Science of the Total Environment, 213:1-3, pp. 57–64.

Mason, R. P., Fitzgerald, W., and Morel, F., 1994.  “The biogeochemical cycling of mercury: Anthropogenic influences,” Geochemica et Cosmochemica Acta, 58:15, pp. 3191–3198.

Mulquiney, J. E., Taylor, J. A., and Norton, J. P. 1993.  “Calculating global atmospheric sources and sinks of greenhouse gases using concentration measurements and chemical models,” in Modelling Change in Environmental Systems, A.J. Jakeman (ed.), John Wiley and Sons, London.

Olmez, I., Ames, M.R., and Gullu, G., 1998 (Oct. 15).  “Canadian and U.S. sources impacting the mercury levels in fine atmospheric particulate material across New York State,” Environmental Science & Technology, 32:20, pp. 3048–3054.

Pai, P., Heisler, S., and Joshi, A., 1998 (Jan.).  “An emissions inventory for regional atmospheric modeling of mercury,” Water Air and Soil Pollution, 101:1-4, pp. 289–308.

Petersen, G., Munthe, J., Pleijel, K., Bloxam, R., and Kumar, A. V., 1998 (March).  “A comprehensive Eulerian modeling framework for airborne mercury species:  Development and testing of the Tropospheric Chemistry Module (TCM),” Atmospheric Environment, 32:5, pp. 829–843.

Pinkney, A. E., Logan, D. T., and Wilson, H. T., 1997 (Aug.).  “Mercury concentrations in pond fish in relation to a coal-fired power plant,” Archives of Environmental Contamination and Toxicology, 33:2, pp. 222–229.

Pirrone, N., et al., 1996 (Sept.).  “Regional differences in worldwide emissions of mercury to the atmosphere,” Atmospheric Environment, 30:17, pp. 2981–2987.

Richaud, R., et al., 1998 (April).  “Trace mercury concentrations in coals and coal-derived material determined by atomic absorption spectrophotometry,” Fuel, 77:5, pp. 359–368.

Schroeder, W. H., and Munthe, J., 1998 (Mar.).  “Atmospheric mercury—An overview,” Atmospheric Environment, 32:5, pp. 809–822.

Shannon, J. D., and Voldner, E. C., 1995.  “Modeling atmospheric concentrations of mercury and deposition to the Great Lakes,” Atmospheric Environment, 29, pp. 1649–1661.

Shia, R., Seigneur, C., Pai, P., Ko, M., and N. Sze, N., “Global Simulation of atmospheric mercury concentrations and deposition fluxes,” Journal of Geophysical Research, 104, pp. 747–760.

Taylor, J. A., 1989.  “A stochastic Lagrangian atmospheric transport model to determine global CO2 sources and sinks:  A preliminary discussion,” Tellus, 41B, pp. 272–285.

Taylor, J. A., 1990.  “New approaches to modelling the global distribution of trace gases in the troposphere,” Mathematics and Computers in Simulation, 32, pp. 59–64.

Taylor, J. A., 1992.  “A global three-dimensional Lagrangian tracer transport modelling study of the sources and sinks of nitrous oxide,”  Mathematics and Computers in Simulation, 33,  pp. 597–602.

Taylor, J. A., 1995.  “Global Carbon Dioxide Sinks:  An investigation of the role of the biosphere in the tropics and middle to high latitudes in the Northern Hemisphere,” in Proceedings of the International Congress on Modelling and Simulation, Newcastle, 27-30 Nov., Vol. II, pp. 39–44.

Taylor, J. A., 1996. “Fossil fuel emissions required to achieve atmospheric stabilization using ANU-BACE:  A box diffusion carbon cycle model,” Ecological Modelling, 86, pp. 195-199.

Taylor, J. A., and Lloyd, J. L., 1992. “Sources and sinks of atmospheric CO2,” Australian Journal of Botany, 40, pp. 407–418.

Taylor, J. A., Brasseur, G., Zimmerman, P., and Cicerone, R., 1991. “A study of the sources and sinks of methane using a global 3-d Lagrangian tropospheric tracer transport model,” Journal of Geophysical Research, 96, pp. 3013–3044.

Taylor, J. A., Zimmerman, P. R., and Erickson, D. J., III, 1996.  “A 3-D modelling study of the sources and sinks of atmospheric carbon monoxide,” Ecological Modelling, 88, pp. 53–71.

Vasiliev, O., Obolenskiy, A.A., and Yagolnitser, M.A., 1998 (June 10).  “Mercury as a pollutant in Siberia:  Sources, fluxes, and a regional budget,” Science of the Total Environment, 213:1–3, pp. 73–84.

Vorres, K., 1990.  “The Argonne Premium Coal Sample Program,” Energy & Fuels, 4:5, pp. 420–426.